## Slide 1: Design Of FIR Filter Design
Module :5 Week 10

## Slide 2: FIR Filter design
FIR filter design is simply to determine the M coefficients of h(n) , n = 0,1, … M-1. from the specification of the desired frequency response H(ω)

## Slide 3: FIR filters using Windows
Let desired frequency response Hd(ω)
The corresponding impulse response hd(n)
Hd(ω) is nothing but Fourier transform of hd(n)
Fourier transform
Inverse Fourier transform

## Slide 4: FIR filters using Windows (contd)
In general, the obtained impulse response is infinite in duration, it must be truncated at some point
That point is n = M-1 to yield an FIR filter length M
This is equivalent to multiplying hd(n) by a “rectangular window” which is

## Slide 5: FIR filters using Windows (contd)
The unit impulse response of the FIR filter becomes

## Slide 6: FIR filters using Windows (contd)
Multiplication in time domain result in convolution of H(ω) with W(ω) in frequency domain
Rectangular window frequency response W(ω)

## Slide 7: Response of Rectangular window
Width of the main lobe is 4π/M
As M increases, main lobe width decreases
Even though the width of the side lobe decreases, the height of the side lobe increase while M increasing
Not visible, because w(ω) has been normalized by M

## Slide 8: Observation from Windows
FIR filter response obtained by truncating hd(n) to length M, plays significant role
Convolution of Hd(ω) with W(ω) has effect if smoothing Hd(ω)
As M increases, W(ω) becomes narrower and smoothing provided by W(ω) is reduced
On the other hand, the large side lobes [w(ω)] result in undesirable ringing effects in the FIR filter frequency response H(ω) and also relatively larger side lobes in H(ω)
FIR filter response obtained by truncating hd(n) to length M, plays significant role
Convolution of Hd(ω) with W(ω) has effect if smoothing Hd(ω)
As M increases, W(ω) becomes narrower and smoothing provided by W(ω) is reduced
On the other hand, the large side lobes [w(ω)] result in undesirable ringing effects in the FIR filter frequency response H(ω) and also relatively larger side lobes in H(ω)

## Slide 9
Name of the Window | Window Sequence
Rectangular | 
Hanning | (or)
Hamming | (or)
Blackman | 
Kaiser | 
Name of the Window | Window Sequence
Rectangular | 
Hanning | 
Hamming | 
Blackman | 
Kaiser | 
Window sequences for FIR filter design

## Slide 10: Time domain and frequency domain characteristics of windows
Hamming window

## Slide 11
Hanning window
Kaiser window
Blackman window

## Slide 12: Windows Observation
All these windows have significantly lower side lobes than rectangular window
Also for the same value of M, the width of the main lobe is wider for other windows compared to rectangular window
The transition in FIR filter response is wider
To reduce the width of the transition region we can increase the length of the window

## Slide 13: Filter Observation
Magnitude response H(ω) of the LPF for M= 61 and M=101 are given below

## Slide 14: Filter Observation
Large oscillations or ripples occur in the pass band of the filter as M increases
Large oscillations are due to large side lobes in frequency characteristic W(ω) of rectangular window
  Due to convolution of W(ω) and Hd(ω), the oscillations occur as side lobes of W(ω) move across the discontinuity exists in Hd(ω)
The multiplication of hd(n) with W(n) is identical to truncating the desired filter characteristic Hd(ω)

## Slide 15: Filter Observation
The truncation introduce ripples in frequency response characteristic of H (ω) due to non uniform convergence
The oscillatory behavior near the band edge of the filter is called Gibbs phenomenon
To avoid this use other windows which has taper and decays towards zero gradually instead of abruptly

## Slide 16
Type of Window | Width of Mainlobe | Peak Sidelobe magnitude (dB)
Rectangular | 4π/M | -13
Hanning | 8π/M | -31
Hamming | 8π/M | -41
Blackman | 12π/M | -58
Kaiser | 4.25π/M | -13.32
Frequency domain Characteristics of some window function

## Slide 17
Type of Filter | Ideal(Desired) Impulse Response
Low Pass Filter | dω : -π ≤ ω < -ωc and ωc < ω < π
High Pass Filter | dω + dω : -ωc < ω < ωc
Band Pass Filter | dω + dω : -π ≤ ω < -ωc2 ; -ωc1 < ω < ωc1 and ωc2 < ω < π
Band stop Filter | dω + dω +dω : -ωc2 < ω < ωc1 and ωc1 < ω < ωc2
Type of Filter | Ideal(Desired) Impulse Response
Low Pass Filter | 
High Pass Filter | 
Band Pass Filter | 
Band stop Filter | 
Desired impulse response for FIR filter design using windows

## Slide 18
Low pass Filter
Band Stop Filter
Band Pass Filter
High pass Filter