## Slide 1
Lecture 1
Introduction to Digital Signal Processing
Dr K. Mohanaprasad
Associate Professor
School of Electronics Engineering (SENSE)
VIT Chennai

## Slide 2
Analog Vs Digital
i) Signal
Analog : voice, audio, video, ….
Digital : digitized analog signal, data
ii) Processing
Analog : passive/active filtering
AM, FM, PM modulation
Fourier, Lap lace transform
Digital : FIR/IIR filtering
AM, windowing
Discrete Fourier transform, z-transform

## Slide 3
Analog vs. Digital (cont’d)
iii) System
Analog : R, L, C, Op-amp, switch, …
Digital : adder, multiplier, memory, …
differential equation
difference equation
iv) Theory
Circuit theory
DSP theory

## Slide 4: What is Signal Processing?
Example of Signals:
  Analog: Speech, Music, Photos, Video, radar, sonar, …
  Discrete-domain/Digital:
    digitized speech, digitized music, digitized images, digitized video, digitized radar and sonar signals,…
    stock market data, daily max temperature data, ...
Processing
Signal in
Signal out
Operation, Transformation
(Analog or Digital)
(Analog or Digital)

## Slide 5: Limitations of Analog Signal Processing
Accuracy limitations due to
  Component tolerances
  Undesired nonlinearities
Limited repeatability due to
  Tolerances
  Changes in environmental conditions
    Temperature
    Vibration
Sensitivity to electrical noise
Limited dynamic range for voltage and currents
Inflexibility to changes
Difficulty of implementing certain operations
  Nonlinear operations
  Time-varying operations
Difficulty of storing information

## Slide 6: Why Go Digital?
Programmability
  One hardware can perform several tasks.
  Upgradeability and flexibility.
Repeatability
  Identical performance from unit to unit.
  No drift in performance due to temperature or aging.
Immune to noise
Offers higher performance.

## Slide 7: Digital Signal Processing
Represent signals by a sequence of numbers
  Sampling or analog-to-digital conversions
Perform processing on these numbers with a digital processor
  Digital signal processing
Reconstruct analog signal from processed numbers
  Reconstruction or digital-to-analog conversion
A/D
DSP
D/A
analog
signal
analog
signal
digital signal
digital signal
Analog input – analog output
  Digital recording of music
Analog input – digital output
  Touch tone phone dialing
Digital input – analog output
  Text to speech
Digital input – digital output
  Compression of a file on computer

## Slide 8: Signals

## Slide 9
Advantages
  Accuracy can be controlled by choosing word length
  Repeatable
  Sensitivity to electrical noise is minimal
  Dynamic range can be controlled using floating point numbers
  Flexibility can be achieved with software implementations
  Non-linear and time-varying operations are easier to implement
  Digital storage is cheap
  Digital information can be encrypted for security
  Price/performance and reduced time-to-market
Limitations
  Sampling causes loss of information
  A/D and D/A requires mixed-signal hardware
  Limited speed of processors
  Quantization and round-off errors

## Slide 10: What is DSP Used For?
…And much more!

## Slide 11: DSP is Everywhere
Sound applications
  Compression, enhancement, special effects, synthesis, recognition, echo cancellation,…
  Cell Phones, MP3 Players, Movies, Dictation, Text-to-speech,…
Communication
  Modulation, coding, detection, equalization, echo cancellation,…
  Cell Phones, dial-up modem, DSL modem, Satellite Receiver,…
Automotive
  ABS, GPS, Active Noise Cancellation, Cruise Control, Parking,…
Medical
  Magnetic Resonance, Tomography, Electrocardiogram,…
Military
  Radar, Sonar, Space photographs, remote sensing,…
Image and Video Applications
  DVD, JPEG, Movie special effects, video conferencing,…
Mechanical
  Motor control, process control, oil and mineral prospecting,…

## Slide 12: Signal Processing Applications
Speech processing
  Speech compression
  Speech recognition
  Speaker Identification, Verification
  Speech synthesis
  Speech enhancement, Echo cancellation

## Slide 13: DSP Applications – Image Processing
Image Processing
  Image compression
  Pattern recognition
  Ghost cancellation
  Noise reduction
  Deblurring
  Object tracking
  Image fusion
Video Processing/compression, tracking...