## Slide 1
Lecture 7
Discrete Fourier Transform (DFT)
Dr K. Mohanaprasad
Associate Professor
School of Electronics Engineering (SENSE)
VIT Chennai

## Slide 2: Introduction to Discrete Time Fourier Transform
Similar to Continuous Time (CT) signals, the Discrete Time (DT) signals or sequences can also be periodic or non-periodic
Periodic or non-periodic DT sequences result in DTFS or DTFT respectively
DTFT is important since most of the signals in engineering applications are non-periodic
DTFT is denoted as ) or simply )
Also x[n] and ) are FT pairs

## Slide 3: Discrete Time Fourier Transform (DTFT)
Mathematical tool for analysis of DT Aperiodic signals is DTFT
DTFT Analysis equation
)
) =
DTFT Synthesis equation
dω

## Slide 4: Discrete Fourier Transform (DFT)
Frequency analysis of DT signals is usually performed on a Digital Signal Processor
Convert time-domain sequence into an equivalent frequency-domain representation
The sampled DTFT of a finite length DT signal is known as DFT
DFT is representation of a sequence x[n] by samples of its spectrum X()
Definition - The simplest relation between a length-N
sequence x[n], defined for 0 ≤ n ≤ N-1, and its DTFT X(ω)
is obtained by uniformly sampling X(ω) on the ω-axis
0 ≤ ω ≤ 2π at ωk=2πk/N
0 ≤ k ≤ N-1

## Slide 5: DFT evolving from DTFT
DFT is a powerful computational tool for Frequency analysis of DT signals.
Consider a DT signal x[n] having a finite duration, in the range N-1, DTFT of this signal is
) = ………..(1)
Sample X() using a total of N equally spaced samples in: ϵ (0, 2π).
The sampling interval is 2π/N

## Slide 6: DFT from DTFT (continued)
Sample X() using the frequencies,
= k = 2πk/N , where N-1
Now ) =
i.e. ) = …… (2)
Eqn.(2) is known as N-point DFT analysis eqn.
To recover the sequence x[n] from X() is IDFT
……(3)
where N-1

## Slide 7: Relation between DTFT and DFT
DTFT is a continuous transform. Sampling the DTFT at regularly spaced intervals around the unit circle gives the DFT
The sampling operation in one domain causes the transform in the other domain to be periodic
Similar to reconstructing a CT signal from its samples, DTFT can also be synthesized from its DFT samples
This reconstruction is possible, as long as the no. of points N at which DFT is computed is equal to or larger than the samples of original signal

## Slide 8: DFT and Inverse DFT
Introducing a complex quantity
=
Twiddle factor is periodic with a period N
DFT Definition:
= where 0≤ ≤
Inverse DFT (IDFT) Definition:
where 0≤ ≤

## Slide 9
Computing
DFT
Â Recall the analysis equation:
∑
X [k ] =
x[n] e
, 0 ≤ k ≤ N − 1
− j 2π
8
6
ª For any given k, the DFT is computed by multiplying
each x[n] with each of the complex exponentials
e
− j 2π 5
8
e
ej2πnk/N
and then adding up all these components
ª If, for example, we wish to compute an 8 point
DFT, the complex exponentials are 8 unit vectors
placed at equal distances from each other on the
unit circle
X[0]=x[0]ej0+ x[1]ej0+ x[2]ej0+ x[3]ej0+ x[4]ej0+ x[5]ej0+ x[6]ej0+ x[7]ej0
− j 2π 4
8
e
− j 2π 3
8
e
X[1]=x[0]ej0+x[1]e-j(2π/8).1+x[2]e-j(2π/8).2+x[3]e-j(2π/8).3+x[4]e-j(2π/8).4+x[5]e-j(2π/8).5+x[6]e-j(2π/8).6+x[7]e-j(2π/8).7
X[2]=x[0]ej0+x[1]e-j(2π/8).2+x[2]e-j(2π/8).4+x[3]e-j(2π/8).6+x[4]e-j(2π/8).0+x[5]e-j(2π/8).2+x[6]e-j(2π/8).4+x[7]e-j(2π/8).6
X[3]=x[0]ej0+x[1]e-j(2π/8).3+x[2]e-j(2π/8).6+x[3]e-j(2π/8).1+x[4]e-j(2π/8).4+x[5]e-j(2π/8).7+x[6]e-j(2π/8).2+x[7]e-j(2π/8).5
X[4]=x[0]ej0+x[1]e-j(2π/8).4+x[2]e-j(2π/8).0+x[3]e-j(2π/8).4+x[4]e-j(2π/8).0+x[5]e-j(2π/8).4+x[6]e-j(2π/8).0+x[7]e-j(2π/8).4
X[5]=x[0]ej0+x[1]e-j(2π/8).5+x[2]e-j(2π/8).2+x[3]e-j(2π/8).7+x[4]e-j(2π/8).4+x[5]e-j(2π/8).1+x[6]e-j(2π/8).6+x[7]e-j(2π/8).3
X[6]=x[0]ej0+x[1]e-j(2π/8).6+x[2]e-j(2π/8).4+x[3]e-j(2π/8).2+x[4]e-j(2π/8).0+x[5]e-j(2π/8).6+x[6]e-j(2π/8).4+x[7]e-j(2π/8).2
X[7]=x[0]ej0+x[1]e-j(2π/8).7+x[2]e-j(2π/8).6+x[3]e-j(2π/8).5+x[4]e-j(2π/8).4+x[5]e-j(2π/8).3+x[6]e-j(2π/8).2+x[7]e-j(2π/8).1
2π
e− j 8 7
N −1 − j 2π n k/ N
n=0

## Slide 10: DFT Computation
Eqn.(5) is known as N-point DFT analysis eqn.
Eqn.(6) is N-point DFT synthesis eqn. (expressed in terms of Twiddle factor)
Computation of each point of DFT requires N complex multiplications and (N-1) complex additions
N-point DFT values can be computed in a total of N2 complex multiplications and N(N-1) complex additions

## Slide 11: DFT example Problem
Compute the DFT of x[n] ={1,1,0,0} using formula method?
Solution: Given N=4
DFT is ) =
Now ) =, where k=0,1,2,3
= + +
+
) = 1 + 1
Sub k=0, we get ) = 1 + 1 = 2

## Slide 12: Problem continued
) = 1 + 1 = 1+ {cos π/2 – j sin π/2 }
Therefore ) = 1 – j
) = 1 + 1 = 1 + {cos π – j sin π}
Therefore ) = 1-1- j(0) = 0
) = 1 + 1 = 1+ {cos 3π/2 – j sin 3π/2}
Therefore ) = 1+0- j(-1) = 1+ j
Answer: DFT X(k) = {2, 1 – j, 0, 1+ j}

## Slide 13: DFT as a linear transformation
DFT of a finite length sequence x[n] is
=…..(1), 0≤ ≤
Range (0, N-1) in above eqn. (1)
x(0) + x(1) + ………+ x(N-1)
………+ x(N-1)
………………………………………………………………………………..
………+ x(N-1)
Eq.(1) of DFT can be expressed in matrix form as
= …….(2)

## Slide 14: Matrix relation for computing DFT
From eqn.(2), both X and x are (Nx1) matrices and is an (N x N) square matrix called the DFT matrix
The complete matrix is described by
The elements of are known as Twiddle Factors

## Slide 15
Matrix Computation
of
DFT
Â DFT has a simple matrix implementation: The DFT samples defined by
kn ,
X [k ] =
0 ≤ k ≤ N − 1
x[n]W
∑
n=0
can be expressed in a matrix form
where X=[X[0] X[1] … X[N-1]]T is the vectorized DFT sequence,
x=[x[0] x[1] … x[N-1]]T is the vectorized time domain sequence, and
DN is the NxN DFT matrix
⎡1
⎢1
DN = ⎢1
⎢M
given by
1
W 1
1
1
⎤
L
L
L
O
L
2
W ( N −1)
⎥
W
N
2
N
N
⎢
2( N −1) ⎥
4
WN
WN
WN
⎥
⎥
M
M
M
( N −1)2 ⎥
⎢
( N −1)
2( N −1)
⎣1
WN
WN
WN
⎦
X = DN x
N −1
N

## Slide 16
Matrix Computation
of
IDFT
•
Likewise, the IDFT relation given by
X [k ]W −kn ,
x[n] =
0 ≤ n ≤
N − 1
∑
k =0
can be expressed in matrix form as
N
DN-1
where
is the NxN IDFT matrix
⎡1
⎢1
1
W −1
1
W −2
1
⎤
L
L
L
O
L
W −( N −1)
⎥
N
−2
N
−4
N
−2( N −1) ⎥
⎢
−1
DN = ⎢1
⎢M
⎣1
WN
WN
WN
⎥
⎥
⎥
⎦
M
M
M
−( N −1)2
⎢
−( N −1)
−2( N −1)
WN
WN
WN
Note that DFT and IDFT matrices
are related to each other
DN =
DN
N
−1 1 *
x = D−1X
N −1
N

## Slide 17: DFT matrix method
Compute the 4-point DFT of the sequence
x[n] = {1,2,1,0} ?
Solution: Given N = 4
= 1, = = cos π/2 – j sin π/2 = – j
= ()2 = cos π – j sin π = -1
= ()3 = cos 3π/2 – j sin 3π/2 = –j(-1)=j
=

## Slide 18: DFT matrix method
=
Ans: DFT X(k) = (, , 0, )

## Slide 19: DFT Problems
Find the DFT of a sequence x[n] = {1, 2, 3, 4} using matrix method?
DFT is =, 0≤ ≤
using matrix method, X4 = W4. x4
Answer is X(k) = { 10, -2+2j, -2, -2-2j }

## Slide 20: Matrix relation to compute IDFT
= …..(1)
Therefore = …….(2)
From eqn.(2), is called IDFT matrix
The equation to find IDFT of a sequence X(k)
…….(3), 0≤ ≤
Expressing IDFT in matrix form ….(4)
Comparing Eqn.(2) & Eqn.(4)
we get = ……(5)

## Slide 21: IDFT problem
Compute the IDFT of the 4-point sequence
X(k) = (, , 0, ) using the DFT?
Solution:
Formula to find IDFT
Step 1: Find the complex conjugate of X(k)
That is = , , 0, )
Step 2: Find the DFT of

## Slide 22: IDFT problem
=

## Slide 23
Step 3:
Find the conjugate of the result and divide it by N=4 to get IDFT IDFT {X(k)} = x[n] = (4,8,4,0)* = (4,8,4,0)
Ans: x[n] = (1,2,1,0)